一 指令格式

二 指令及其参数

Data := 	Value

AccSet 	Acc 	Ramp

ActUnit 	MecUnit

Add 		Name 	AddValue

# Break

CallBy Var Name 	Number

Clear 	Name

ClkReset 	Clock

ClkStart 	Clock

ClkStop 	Clock

Close 	IODevice

! Comment

ConfJ 	[\On] | [\Off]

ConfL 	[\On] | [\Off]

CONNECT Interrupt	 WITH 	Trap routine

CorrCon Descr

CorrDiscon Descr

CorrWrite Descr Data

CorrClear

DeactUnit 	MecUnit

Decr 		Name

EOffsSet 	EaxOffs	ErrWrite 	[ \W ] Header Reason

[ \RL2] [ \RL3] [ \RL4]

Exit

ExitCycle

FOR 		Loop counter 	FROM 	Start value 	TO 	End value

[STEP 	Step value] 	DO ... ENDFOR

GOTO 	Label

GripLoad 	Load

IDelete 	Interrupt

IF 		Condition ...

IF 		Condition 	THEN ...

{ELSEIF 	Condition 	THEN ...}

[ELSE ...]

ENDIF

Incr 		Name

IndAMove 	MecUnit Axis [ \ToAbsPos ] | [ \ToAbsNum ] Speed[ \Ramp ]

IndCMove 	MecUnit Axis 	Speed 	[ \Ramp ]

IndDMove 	MecUnit Axis Delta 	Speed 	[ \Ramp ]

IndReset 	MecUnit Axis 	[ \RefPos ] | [ \RefNum ] | [ \Short ] | [ \Fwd ] |[ \Bwd ] | [ \Old ]

IndRMove 	MecUnit Axis [ \ToRelPos ] | [ \ToRelNum ] | [ \Short ] |[ \Fwd ] | [ \Bwd ] 	Speed [ \Ramp ]

InvertDO 	Signal

IODisable 	UnitName 	MaxTime

IOEnable 	UnitName 	MaxTime

ISignalDI 	[ \Single ] 	Signal 	TriggValue 		Interrupt

ISignalDO 	[ \Single ] 	Signal 	TriggValue 		Interrupt

ISleep 	InterruptITimer 		[ \Single ] 		Time Interrupt

IVarValue 	VarNo 	Value, 	Interrupt

IWatch 	Interrupt

Label:

MoveAbsJ [ \Conc ] ToJointPos Speed [ \V ] | [ \T ] Zone [ \Z]Tool

[\WObj ]

MoveC [ \Conc ] CirPoint ToPoint Speed [ \V ] | [ \T ] Zone [ \Z]Tool [

\WObj ]

MoveJ [ \Conc ] ToPoint Speed [ \V ] | [ \T ] Zone [ \Z ] Tool[ \WObj ]

MoveL [ \Conc ] ToPoint Speed [ \V ] | [ \T ] Zone [ \Z ] Tool[ \WObj ]

Open Object [\File] IODevice [\Read] | [\Write] | [\Append] | [\Bin]

PathResol Value

PDispOn [ \Rot ] [ \ExeP ] ProgPoint Tool [ \WObj ]

PDispSet DispFrame

PulseDO [ \PLength ] Signal

RAISE [ Error no ]

Reset Signal

RETURN [ Return value ]

Rewind IODevice

SearchC [ \Stop ] | [ \PStop ] | [ \Sup ] Signal SearchPoint CirPoint

ToPoint Speed [ \V ] | [ \T ] Tool [ \WObj ]

SearchL [ \Stop ] | [ \PStop ] | [ \Sup ] Signal SearchPoint ToPoint

Speed [ \V ] | [ \T ] Tool [ \WObj ]

Set Signal

SetAO Signal ValueSetDO [ \SDelay ] Signal Value

SetGO Signal Value

SingArea [ \Wrist] | [ \Arm] | [ \Off]

SoftAct Axis Softness [\Ramp ]

Stop [ \NoRegain ]

TEST Test data {CASE Test value {, Test value} : ...}

[ DEFAULT: ...] ENDTEST

TPReadFK Answer String FK1 FK2 FK3 FK4 FK5 [\MaxTime]

[\DIBreak] [\BreakFlag]

TPReadNum Answer String [\MaxTime] [\DIBreak] [\BreakFlag]

TPShow Window

TPWrite String [\Num] | [\Bool] | [\Pos] | [\Orient]

TriggC CirPoint ToPoint Speed [ \T ] Trigg_1 [ \T2 ] [ \T3 ][ \T4]

Zone Tool [ \WObj ]

TriggInt TriggData Distance [ \Start ] | [ \Time ] Interrupt

TriggIO TriggData Distance [ \Start ] | [ \Time ] [ \DOp ] | [ \GOp ]

|[\AOp ] SetValue [ \DODelay ] | [ \AORamp ]

TriggJ ToPoint Speed [ \T ] Trigg_1 [ \T2 ] [ \T3] [ \T4]Zone Tool [ \WObj]

TriggL ToPoint Speed [ \T ] Trigg_1 [ \T2] [ \T3] [ \T4]Zone Tool[ \WObj ]

TuneServo MecUnit Axis TuneValue

TuneServo MecUnit Axis TuneValue [\Type]

UnLoad FilePath [\File]

VelSet Override Max

WaitDI Signal Value [\MaxTime] [\TimeFlag]

WaitDO Signal Value [\MaxTime] [\TimeFlag]

WaitTime [\InPos] TimeWaitUntil [\InPos] Cond [\MaxTime] [\TimeFlag]

WHILE Condition DO ... ENDWHILE

Write IODevice String [\Num] | [\Bool] | [\Pos] | [\Orient][\NoNewLine]

WriteBin IODevice Buffer NChar

WriteStrBin IODevice Str

WZBoxDef [\Inside] | [\Outside] Shape LowPoint HighPoint

WZCylDef [\Inside] | [\Outside] Shape CentrePoint Radius

WZDisable WorldZone

WZDOSet [\Temp] | [\Stat] WorldZone [\Inside] | [\Before]

Signal SetValue

WZEnable WorldZone

WZFree WorldZone

WZLimSup [\Temp] | [\Stat] WorldZone Shape

WZSphDef [\Inside] | [\Outside] Shape CentrePoint Radius

三 函数及其参数

Abs (Input)

ACos (Value)

AOutput (Signal)

ArgName (Parameter)

ASin (Value)

ATan (Value)

ATan2 (Y X)

ByteToStr (ByteData [\Hex] | [\Okt] | [\Bin] | [\Char])

ClkRead (Clock) CorrRead

Cos (Angle)

CPos ([Tool] [\WObj])

CRobT ([Tool] [\WObj])

DefDFrame (OldP1 OldP2 OldP3 NewP1 NewP2 NewP3)

DefFrame (NewP1 NewP2 NewP3 [\Origin])

Dim (ArrPar DimNo)

DOutput (Signal)

EulerZYX ([\X] | [\Y] | [\Z] Rotation)

Exp (Exponent)

GOutput (Signal)

GetTime ( [\WDay] | [\Hour] | [\Min] | [\Sec] )

IndInpos MecUnit Axis

IndSpeed MecUnit Axis [\InSpeed] | [\ZeroSpeed]

IsPers (DatObj)

IsVar (DatObj)

MirPos (Point MirPlane [\WObj] [\MirY])

NumToStr (Val Dec [\Exp])

Offs (Point XOffset YOffset ZOffset)

OrientZYX (ZAngle YAngle XAngle)

ORobT (OrgPoint [\InPDisp] | [\InEOffs])

PoseInv (Pose)

PoseMult (Pose1 Pose2)

PoseVect (Pose Pos)

Pow (Base Exponent) Present (OptPar)

ReadBin (IODevice [\Time])

ReadMotor [\MecUnit ]Axis

ReadNum (IODevice [\Time])

ReadStr (IODevice [\Time])

RelTool (Point Dx Dy Dz [\Rx] [\Ry] [\Rz])

Round ( Val [\Dec])

Sin (An gl e )

Sqrt (Value)

StrFind (Str ChPos Set [\NotInSet])

StrLen (Str)

StrMap ( Str FromMap ToMap)

StrMatch (Str ChPos Pattern)

StrMemb (Str ChPos Set)

StrOrder ( Str1 Str2 Order)

StrPart (Str ChPos Len)

StrToByte (ConStr [\Hex] | [\Okt] | [\Bin] | [\Char])

StrToVal ( Str Val )

Tan (Angle)

TestDI (Signal)

Trunc ( Val [\Dec] )

ValToStr ( Val )